## Slide 1: Bluetooth Low Energy Based CoAP Communication in IoT
---- CoAPNonIP: An Architecture Grants CoAP in WPAN
Notes: Introduction and background, including highlights (if any) from lit review (1-2 min.)
Research question (1 min.)
Research design and methods (5 min. max)
Data sources and selection Findings (10 min.) [this should be your main focus]
Recommendations/implications (2-5 min.)
Summary and conclusion (1-2 min.)

## Slide 2: Content
Introduction
Related Works
Problem Definition
Architecture
Experiment
Conclusion
Future Work

## Slide 3: 1 Introduction
1.1 Internet of Things (IoT)
Figure 1: Trend of devices vs people[1]

## Slide 4: 1 Introduction
CoAP is designed for constrained networks under the context of IoT.
1.2 Constrained Application Protocol (CoAP)
Figure 2: CoAP vs HTTP[2]
Notes: CoAP is designed to easily interface with HTTP for integration with the Web while meeting specialized requirements such as
Constrained Application Protocol
Header compression, which compresses the 40-byte IPv6 and 8-byte UDP headers by assuming the usage of common fields.
Fragmentation and reassembly, as the data link of IEEE 802.15.4 with a frame length of max 127 bytes does not match the MTU of IPv6, which is 1280 bytes.
Stateless auto configuration, the process where devices inside the 6LoWPAN network automatically generate their own IPv6 address.
ARM(British multinational semiconductor and software design company )
//multicast support,
//very low overhead,
//simplicity for constrained environments.
//Payload size limited to 1024 bytes.
Multicast: send (data) across a computer network to several users at the same time.

## Slide 5: 2 Related Works
2.1 In terms of IPv6 adoption
In December 2014, Pv6 over Low power Wireless Personal Area Networks (6LoWPAN) is supported by BLE 4.2[3].
Figure 3: IPv6 in BLE Stack[4]
Notes: It provides instructions and URI format for SMS, Websocket and TCP.
CoRE Working Group(Informational document) Internet-Draft
ATT (page 2160): "This specification defines the Attribute Protocol; a protocol for discovering, reading, and writing attributes on a peer device."
GATT (page 2207): "This specification defines the Generic Attribute Profile that describes a service framework using the Attribute Protocol for discovering services, and for reading and writing characteristic values on a peer device."

## Slide 6: 2 Related Works
2.2 In terms of getaway solutions
CoAP gateway for FS20 based home automation[5].
CoAP gateway for DNP3.0 based distribution automation system[6].
CoAP gateway for UPnP and ZigBee bridging[7].
Notes: CoAP gateway for FS20 based home automation: mapping FS20 device address to CoAP resource
June 8,2016, JupiterMesh® Neighborhood Area Network (NAN) Announced
DNP3 (Distributed Network Protocol) is a set of communications protocols used between components in process automation systems. Its main use is in utilities such as electric and water companies. Usage in other industries is not common. It was developed for communications between various types of data acquisition and control equipment. It plays a crucial role in SCADA systems,

## Slide 7: 3 Problem Definition
Motivation: Why devices can not directly send CoAP messages to each other without adding extra hardware layer or adopting protocol translation?
An architecture to make CoAP work on existing communication protocols for WPAN such as BLE and NFC.
Meanwhile, BLE is used to explore how to overcome limitations of underline technologies.
3.1 Proposed solution
Notes: Currently, there are two ways to introduce CoAP in wireless personal area network.
New hardware layer
Protocol transfer at gate way

## Slide 8: 3 Problem Definition
3.2 Problem
How to identify Non-IP based devices?
How to overcome packet size limitation of BLE?
How to serve multiple applications as a background service?
How to provide a common interface to support different technologies?
Notes: Goal 1. A general method to identify Non-IP based devices.
Goal 2. An architecture to support CoAP communication in BLE.
Goal 3. A background service to support multiple apps.
Goal 4. An interface to support other WPAN technologies.

## Slide 9: 4 Architecture
4.1 Overview
Application layer.
Network layer.
Notes: Application layer consists of process component & communication component

## Slide 10: 4 Architecture
4.2 Application layer
Process component:
Processors
Senders
Communication component:
Broadcast
Search peers
Get nodes
Send data
Receive data
Notes: Threads with dispatcher to handle request
Threads with dispatcher to send out request
Customized callback functions to handle responses.

## Slide 11: 4 Architecture
4.3 Network layer – communication mechanism
Figure 4 : Communication mechanism

## Slide 12: 4 Architecture
4.3 Network layer – packet format
Figure 5 : Communication mechanism
Notes: 10min

## Slide 13: 5 Experiment
5.1 Experiment setup
Title | Goals
Minimum Data with Interval | Test performance of sending CoAP header with different intervals.
Multiple Packets | Test performance of sending different CoAP messages with different data size.
Round Trip | Test performance of round trip
Multiple Apps | Test performance of underlying service to support multiple apps
Table 1: Experiment setup

## Slide 14: 5 Experiment
Chart: 
5.2 Experiment 1: Minimum data with interval
Figure 6: Results of sending headers with different interval
Notes: the connection interval is the amount of time between two connection events

## Slide 15: 5 Experiment
Chart: 
5.3 Experiment 2: Multiple packets
Figure 7: Results of sending multiple packets

## Slide 16: 5 Experiment
Chart: 
5.4 Experiment 3: Round trip
Figure 8: First set of 4-byte round trip

## Slide 17: 5 Experiment
Chart: 
Major App | 197.6442 | 196.7178 | 204.6365 | 202.0226 | 201.4354 | 200.4426 | 197.2393 | 198.0713 | 197.8523 | 198.8834
Trigger App | 112.5889 | 132.623 | 122.316 | 138.7521 | 114.7 | 123.9324 | 181.1185 | 113.304 | 114.1639 | 116.3395
5.5 Experiment 4: Multiple apps
Figure 9: Result of Multi-App Experiment

## Slide 18: 5 Experiment
5.6 Conclusion
The data rate is 160 byte/s.
The constant fluctuation comes from save energy mechanisms.
The performance of Android’s peripheral mode needs to be improved.
The competition in the message queue influences the received time of a message.
Notes: “Connection interval” can be any value between 7.5ms and 4s.
The data rate is 160 byte/s. due to wait ACK

## Slide 19: 6 Conclusion
The proposed architecture provides a software solution to enable CoAP communication in WPAN.
Although the research result has been published by IEEE[8] [9], further works need to be done for better performance.
Notes: A general method to identify Non-IP based devices.
An architecture to support CoAP communication in BLE.
A background service to support multiple apps.
An interface to support other WPAN technologies.

## Slide 20: 7 Future works
Data Rate
Availability
Cross-Platform
Underlying Technology
Security

## Slide 21: References
[1] Howard, P. N. (2015, June 9). Sketching out the Internet of Things trendline. Retrieved 6 7, 2016, from http://www.brookings.edu/blogs/techtank/posts/2015/06/9-future-of-iot-part-2
[2] Sutaria, R., & Govindachari, R. (2013, May 1). Understanding The Internet Of Things. Retrieved June 13, 2016, from electronicdesign.com: http://electronicdesign.com/iot/understanding-internet-things
[3] SIG. (2014, December). BLUETOOTH ® CORE SPECIFICATION 4.2 FREQUENTLY ASKED QUESTIONS. Retrieved April 18, 2016, from bluetooth.org: https://www.bluetooth.org/ja-jp/Documents/Bluetooth4-2FAQ.pdf
[4] Isomaki, M., Nieminen, J., Gomez, C., Shelby, Z., Savolainen, T., & Patil, B. (2015, October). IPv6 over BLUETOOTH(R) Low Energy. Retrieved June 7, 2016, from ietf.org: https://tools.ietf.org/html/rfc7668
[5] Bergmann, O., Hillmann, K. T., & Gerdes, S. . (2012). A CoAP-gateway for smart homes. Computing, Networking and Communications (ICNC), 2012 International Conference on (pp. 446-450). Maui, HI: IEEE.
Notes: [5] Bergmann, O., Hillmann, K. T., & Gerdes, S. , 2012
[6] Shin, I. J., Eom, D. S., & Song, B. K., 2015
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T., 2011

## Slide 22: References
[6] Shin, I. J., Eom, D. S., & Song, B. K. (2015). The CoAP-based M2M gateway for distribution automation system using DNP3.0 in smart grid environment. 2015 IEEE International Conference on Smart Grid Communications (SmartGridComm) (pp. 713-718). Miami, FL: IEEE.
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T. (2011). Bridging UPnP and ZigBee with CoAP: Protocol and its Performance Evaluation. IoTSP '11 Proceedings of the workshop on Internet of Things and Service Platforms (p. 1). ACM.
[8] Chen, N., Li, X., & Deters, R. (2015). Collaboration & Mobile Cloud-Computing: Using CoAP to Enable Resource-Sharing between Clouds of Mobile Devices. 2015 IEEE Conference on Collaboration and Internet Computing (CIC) (pp. 119 - 124). Hangzhou: IEEE.
[9] Shi, H., Chen, N., & Deters, R. (2015). Combining Mobile and Fog Computing: Using CoAP to Link Mobile Device Clouds with Fog Computing. 2015 IEEE International Conference on Data Science and Data Intensive Systems (pp. 564 - 571). Sydney: IEEE.
Notes: [5] Bergmann, O., Hillmann, K. T., & Gerdes, S. , 2012
[6] Shin, I. J., Eom, D. S., & Song, B. K., 2015
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T., 2011

## Slide 23
Thank you