## Slide 1: Bluetooth Low Energy Based CoAP Communication in IoT
---- CoAPNonIP: An Architecture Grants CoAP in WPAN
Notes: Introduction and background, including highlights (if any) from lit review (1-2 min.)
Research question (1 min.)
Research design and methods (5 min. max)
Data sources and selection Findings (10 min.) [this should be your main focus]
Recommendations/implications (2-5 min.)
Summary and conclusion (1-2 min.)
The topic of my thesis is ********************

## Slide 2: Content
Introduction
Problem Definition
Related Works
Architecture
Experiment
Conclusion
Future Work
Notes: In term of content,
First, I will introduce the trend of IoT and the importance of CoAP.
Then, I will discuess related works before dive deep into architecture & experiment.
Last, I will make conclusion & discuss future works.

## Slide 3: 1 Introduction
1.1 Internet of Things (IoT)
Figure 1: Trend of devices vs people[1]
Notes: According to Howard in 2015, the number of devices in IoT has exceed the polulation of human being before 2015. And most predictions expect the trend of exponential growth will keep in the next 2 decades.

## Slide 4: 1 Introduction
CoAP is a light version of HTTP.
1.2 Constrained Application Protocol (CoAP)
Figure 2: CoAP vs HTTP[2]
Notes: In terms of CoAP, It has inherent many characteristics from HTTP. Like http verbs and attributes of HTTP header.
By default it adopt the UDP in transport layer & 6lowpan in network layer.
Since 6lowpan is a very important alternative of IPv6 in constrained networks, I will discuss it later.
IPv6 in low power wireless personal area networks.
//multicast support,
//very low overhead,
//simplicity for constrained environments.
//Payload size limited to 1024 bytes.
Constrained Application Protocol
Header compression, which compresses the 40-byte IPv6 and 8-byte UDP headers by assuming the usage of common fields.
Fragmentation and reassembly, as the data link of IEEE 802.15.4 with a frame length of max 127 bytes does not match the MTU of IPv6, which is 1280 bytes.
Stateless auto configuration, the process where devices inside the 6LoWPAN network automatically generate their own IPv6 address.
ARM(British multinational semiconductor and software design company )
Multicast: send (data) across a computer network to several users at the same time.

## Slide 5: 3 Problem Definition
Send CoAP message through BLE
3.1 Motivation
Sensor
Gateway
Sensor
HTTP
Server
HTTP
Server
Gateway
CoAP over IP
CoAP over BLE ?
Figure 3: Context of CoAP
Notes: After review the characteristics of CoAP, I was thinking why we can’t make CoAP get ride of the constrains in IP protocols & make is works on technology like BLE.

## Slide 6: 3 Problem Definition
3.2 Problem
How to identify Non-IP based devices?
How to overcome packet size limitation of BLE?
How to serve multiple applications as a background service?
How to provide a common interface to support different technologies?
Notes: Goal 1. A general method to identify Non-IP based devices.
Goal 2. An architecture to support CoAP communication in BLE.
Goal 3. A background service to support multiple apps.
Goal 4. An interface to support other WPAN technologies.
After propoed those 4 questions I go to review relative works.

## Slide 7: 2 Related Works
2.1 In terms of IPv6 adoption
6LoWPAN is adopted by BLE in Bluetooth core specification 4.2[3].
Figure 4: IPv6 in BLE Stack[4]
Notes: In December 2014, IPv6 over Low power Wireless Personal Area Networks (6LoWPAN) is supported by BLE 4.2[3].
Isomaki
As shown in this chart besides the traditional “Generic Attribute Profile” protocol stacks. The new architecture of BLE adopt 6lowpan upon
The Logical Link Control and Adaptation.
In this way, by adding new hardware, the CoAP can be used in BLE.
It provides instructions and URI format for SMS, Websocket and TCP.
CoRE Working Group(Informational document) Internet-Draft
ATT (page 2160): "This specification defines the Attribute Protocol; a protocol for discovering, reading, and writing attributes on a peer device."
GATT (page 2207): "This specification defines the Generic Attribute Profile that describes a service framework using the Attribute Protocol for discovering services, and for reading and writing characteristic values on a peer device."

## Slide 8: 2 Related Works
2.2 In terms of getaway solutions
CoAP gateway for FS20 based home automation[5].
CoAP gateway for DNP3.0 based automation system[6].
CoAP gateway for bridging UPnP and ZigBee [7].
Notes: Also, we see the CoAP are used as a gateway protocol between contained netoworks and the Internet. As shown here, Iisted three resent researches which are all using CoAP at the GateWay.
Also, CoAP gateways are used to make protocol translation between CoAP network and WPAN. Here I list three related researches.
Extended CoAP Codes to incorporate UPnP(Universal Plug and Play
) controls. Leave is issued by a sensor device when it leaves UPnP. Alive, Ping and CollectAll are for management of UPnP.
June 8,2016, JupiterMesh® Neighborhood Area Network (NAN) Announced
DNP3 (Distributed Network Protocol) is a set of communications protocols used between components in process automation systems. Its main use is in utilities such as electric and water companies. Usage in other industries is not common. It was developed for communications between various types of data acquisition and control equipment. It plays a crucial role in SCADA systems,

## Slide 9: 2 Related Works
2.3 Conclustion
No software architecture for CoAP communication in BLE netoworks.
Notes: After review the use of CoAP in IoT. My conclusion is thereis not software architecture for CoAP communication in BLE netowork.
Then, I turn to design the software solution.

## Slide 10: 4 Architecture
4.1 Overview
Application layer
Network layer
Figure 5: Overview of architectrue
Process component
Communication component
Network component
Notes: As you can see, in brief, the archictrue consists of application layer & network layer.

## Slide 11: 4 Architecture
4.2 Application layer
Process component:
Processors
Senders
Communication component:
Broadcast
Search peers
Get nodes
Send data
Receive data
Notes: Threads with dispatcher to handle request
Threads with dispatcher to send out request
Customized callback functions to handle responses.

## Slide 12: 4 Architecture
4.3 Network layer – communication mechanism
Figure 6 : Communication mechanism

## Slide 13: 4 Architecture
4.3 Network layer – packet format
Figure 7 : Communication mechanism
Notes: 10min

## Slide 14: 5 Experiment
5.1 Experiment setup
Title | Goals
CoAP header with Interval | Test performance of sending CoAP header with different intervals.
Multiple Packets | Test performance of sending different CoAP messages with different data size.
Round Trip | Test performance of round trip
Multiple Apps | Test performance of underlying service to support multiple apps
Table 1: Experiment setup

## Slide 15: 5 Experiment
5.1 Experiment setup
Figure 8: Screenshot
Notes: Android OS, v5.1.1(Lollipop)
Dual-core 2.3 GHz Denver
16GB/2GB RAM
Bluetooth v4.1, A2DP, apt-X

## Slide 16: 5 Experiment
Chart: 
5.2 Experiment 1: Minimum data with interval
Figure 9: Results of sending headers with different interval
Notes: the connection interval is the amount of time between two connection events. The device has a minimum and a maximum value for it. Which Android API does not provide.
// 1. The time cost of sending a BLE packet is around 100ms. (in android)
// 2. With the increase of interval the heart-beat like pattern appears more frequently. (Due to BLE’s strategies for saving energy)
// 3. There are some random fluctuation (Android’s BLE implementation)

## Slide 17: 5 Experiment
Chart: 
5.3 Experiment 2: Multiple packets
Figure 10: Results of sending multiple packets
Notes: The implementation used a synchronized way to exchange data.

## Slide 18: 5 Experiment
5.4 Experiment 3: Round trip
Figure 11: 4-byte round trip
Notes: The main limitation of communication is the time window of a data exchange event.

## Slide 19: 5 Experiment
Chart: 
Major App | 197.6442 | 196.7178 | 204.6365 | 202.0226 | 201.4354 | 200.4426 | 197.2393 | 198.0713 | 197.8523 | 198.8834
Trigger App | 112.5889 | 132.623 | 122.316 | 138.7521 | 114.7 | 123.9324 | 181.1185 | 113.304 | 114.1639 | 116.3395
5.5 Experiment 4: Multiple apps
Figure 12: Result of Multi-App Experiment

## Slide 20: 5 Experiment
5.6 Conclusion
Data rate = 160 byte/s.
Energy-saving mechanisms of BLE influence results.
Android’s implementation of BLE influences results.
The single communication channel is a restriction.
Notes: “Connection interval” can be any value between 7.5ms and 4s.
The data rate is 160 byte/s. due to wait ACK

## Slide 21: 6 Conclusion
The proposed architecture provides a software solution to enable CoAP communication in WPAN.
The research results have been published by IEEE[8] [9].
Notes: A general method to identify Non-IP based devices.
An architecture to support CoAP communication in BLE.
A background service to support multiple apps.
An interface to support other WPAN technologies.

## Slide 22: 7 Future works
Data Rate
Availability
Cross-Platform
Underlying Technology
Security

## Slide 23: References
[1] Howard, P. N. (2015, June 9). Sketching out the Internet of Things trendline. Retrieved 6 7, 2016, from http://www.brookings.edu/blogs/techtank/posts/2015/06/9-future-of-iot-part-2
[2] Sutaria, R., & Govindachari, R. (2013, May 1). Understanding The Internet Of Things. Retrieved June 13, 2016, from electronicdesign.com: http://electronicdesign.com/iot/understanding-internet-things
[3] SIG. (2014, December). BLUETOOTH ® CORE SPECIFICATION 4.2 FREQUENTLY ASKED QUESTIONS. Retrieved April 18, 2016, from bluetooth.org: https://www.bluetooth.org/ja-jp/Documents/Bluetooth4-2FAQ.pdf
[4] Isomaki, M., Nieminen, J., Gomez, C., Shelby, Z., Savolainen, T., & Patil, B. (2015, October). IPv6 over BLUETOOTH(R) Low Energy. Retrieved June 7, 2016, from ietf.org: https://tools.ietf.org/html/rfc7668
[5] Bergmann, O., Hillmann, K. T., & Gerdes, S. . (2012). A CoAP-gateway for smart homes. Computing, Networking and Communications (ICNC), 2012 International Conference on (pp. 446-450). Maui, HI: IEEE.
Notes: [5] Bergmann, O., Hillmann, K. T., & Gerdes, S. , 2012
[6] Shin, I. J., Eom, D. S., & Song, B. K., 2015
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T., 2011

## Slide 24: References
[6] Shin, I. J., Eom, D. S., & Song, B. K. (2015). The CoAP-based M2M gateway for distribution automation system using DNP3.0 in smart grid environment. 2015 IEEE International Conference on Smart Grid Communications (SmartGridComm) (pp. 713-718). Miami, FL: IEEE.
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T. (2011). Bridging UPnP and ZigBee with CoAP: Protocol and its Performance Evaluation. IoTSP '11 Proceedings of the workshop on Internet of Things and Service Platforms (p. 1). ACM.
[8] Chen, N., Li, X., & Deters, R. (2015). Collaboration & Mobile Cloud-Computing: Using CoAP to Enable Resource-Sharing between Clouds of Mobile Devices. 2015 IEEE Conference on Collaboration and Internet Computing (CIC) (pp. 119 - 124). Hangzhou: IEEE.
[9] Shi, H., Chen, N., & Deters, R. (2015). Combining Mobile and Fog Computing: Using CoAP to Link Mobile Device Clouds with Fog Computing. 2015 IEEE International Conference on Data Science and Data Intensive Systems (pp. 564 - 571). Sydney: IEEE.
Notes: [5] Bergmann, O., Hillmann, K. T., & Gerdes, S. , 2012
[6] Shin, I. J., Eom, D. S., & Song, B. K., 2015
[7] Mitsugi, J., Yonemura, S., Hada, H., & Inaba, T., 2011

## Slide 25
Thank you